## Slide 1
Low-Cost Intelligent Real-Time ECG Monitoring System Using Artificial Intelligence
Guilherme Martins Specht
Prof. Laurent Latorre
MEA4
05/06/2026
Université de Montpellier / Polytech Montpellier

## Slide 2
Cardiovascular diseases are leading causes of death
Need for rapid ECG interpretation
Lack of low-cost intelligent systems
Importance in emergency and remote environments
Motivation

## Slide 3
Problem Statement
How to develop a low-cost embedded system capable of:
acquiring ECG signals,
processing them in real time,
and classifying cardiac rhythms using AI?

## Slide 4
Objectives
General objective
  Develop a real-time intelligent ECG monitor
Specific objectives
  Acquire ECG with AD8232
  Process ECG digitally
  Detect R-peaks
  Calculate BPM and RR
  Classify rhythms using CNN
  Create real-time monitoring interface

## Slide 5
ECG Fundamentals
Image ECG:
  P wave
  QRS complex
  T wave

## Slide 6
Cardiac Arrhythmias
RHYTHM | BPM
Bradycardia | < 60
Normal | 60 - 100
Tachycardia | > 100

## Slide 7
Components Used
ESP32-S3
AD8232
ADS1115
OLED

## Slide 8
System Architecture

## Slide 9
Signal Processing
Pipeline:
  Raw ECG: Original electrical cardiac signal acquired from the electrodes, still containing noise and baseline variations. ↓ Derivative: Emphasizes rapid signal changes, helping to highlight the QRS complex. ↓ Squaring: Squares the signal values, enhancing large peaks and making all values positive. ↓ Moving Window Integration: Smooths the processed signal and emphasizes regions where heartbeats occur. ↓ Adaptive Threshold: Dynamically adjusts the detection threshold to distinguish real heartbeats from noise. ↓ R-Peak Detection: Identifies R peaks, which are used to calculate RR intervals, BPM, and support arrhythmia classification.

## Slide 10
Signal Processing
Pipeline:
  Raw ECG: ↓ Derivative: ↓ Squaring: ↓ Moving Window Integration: ↓ Adaptive Threshold: ↓ R-Peak Detection:

## Slide 11
Artificial Intelligence
1D CNN
MIT-BIH dataset
Synthetic signals
Real-time classification

## Slide 12
CNN Architecture
Conv1D: Extracts local patterns from the ECG signal, such as QRS morphology and waveform variations. ↓ MaxPooling: Reduces the signal size while keeping the most important features. ↓ Conv1D: Extracts deeper and more complex ECG features from the previous layer. ↓ Dense: Combines the extracted features to support the final rhythm decision. ↓ Softmax: Converts the final outputs into class probabilities, indicating the most likely ECG class.

## Slide 13
RESULTS
LEARN
MIT-BIH DATABASE
DETECT
PAN-TOMPKINS
RESULTS

## Slide 14
AI Results
CNN test set: MIT-BIH ECG windows
Final accuracy: 90.63%
Best performance: normal and ventricular classes
Limitation: minority classes affected by imbalance

## Slide 15
Real-Time Monitor

## Slide 16
Real-Time Monitor

## Slide 17
Future Work & Limitations
Development of a PCB;
Using a finger sensor;
Improving the analog front-end and electrode connection stability;
Using better filtering techniques for noise reduction;
Increasing the number of real ECG acquisitions;
Balancing the CNN dataset;
Improving classification of minority classes;
Deploying TinyML inference directly on the ESP32-S3;
Using MQTT, BLE, or WiFi communication;
Developing a mobile application;
Performing validation with controlled biomedical datasets;
Investigating clinical validation in partnership with healthcare professionals.
Noise sensitivity
No clinical validation
Limited dataset

## Slide 18
Conclusion
Functional system
Real-time ECG monitoring
AI-assisted analysis
Low-cost architecture